A Constraint Logic Programming Framework
for the Synthesis of Fault-Tolerant Schedules
for Distributed Embedded Systems
Fault-tolerance
Fault-tolerant scheduling
More complex scheduling schemes yield more slack for energy management
  - Trade-off transparency for performance
  - Performance, and hence the obtainable energy savings are greatly increased
More complex schemes demand larger schedule tables to be stored in the processing elements, and more sophisticated online schedulers
Reliable energy management
System reliability is affected by use of energy management
  - The use of DVS increases the probability of faults, thus damaging the system reliability
Reliability must be considered in the optimisation process
  - Considering reliability in the optimisation process allows for finding the minimum energy schedule that meets the reliability goal
  - Reliability is imposed as a constraint
Reliability can be met at very little energy cost
  - Considering the reliability while optimising enables us to find reliable schedules with comparable energy savings
Design optimisation tool
for distributed embedded real-time systems
Decides mapping, fault-tolerance policy and fault-tolerant schedule
  - Hard real-time,
  - Hard reliability goal,
  - Static schedule for processes and messages,
  - Fault-tolerance for k transient/soft faults
Optimise for minimal energy consumption
While considering impact of lowering voltages on the probability of faults
Constraint logic programming (CLP) based implementation
Message
Optimising naively for energy will destroy reliability
Considering reliability as hard design constraint allows for carefully doing design optimisation such that reliability is guaranteed, and energy consumption is minimised comparably
Faults are tolerated by using temporal or spatial redundancy, or a combination of the two
Replication
Re-execution
Energy vs. reliability
Passive Replication
Energy vs. faults
Lowering voltage decreases critical energy of circuit.
Probability of transient faults increase.
Relation is expressed as1:
λ(f)=λ_0 10^{{d(1-f)} over {1-f_{min}} }
Reliability for energy trade-off
Failure rate vs. Voltage
Relative voltage
Increase in fault rate
Relation between voltage and failure rate1
1 Source: D. Zhu et al.: “Reliability-Aware Energy Management for Periodic Real-Time Tasks”, 2007
IMM / Informatics and Mathematical Modelling Embedded Systems Engineering eselab.imm.dtu.dk
PE2
PE1
P1
P1
PE2
PE1
P1
P1
PE2
PE1
P1
P1
63% E0
PE2
PE1
P1
P3
P5
Bus
1
2
P2
P4
PE2
PE1
P1
P2
P4
P3
P5
Bus
1
2
P3
P4/5
PE2
PE1
P1
P2
P4
P3
P5
Bus
1
2
P1
P2
P4
P3
P5
Fully Transparent Scheduling
Deadline
100% E0
38% E0
Conditional Scheduling
Slack Sharing Scheduling
P1
P2
P3
P4
P5
PE1
PE2
P
1
40
40
P
2
40
40
P
3
30
30
P
4
40
40
P
5
40
40
PE
1
PE
2
m1
m2
k=1
Comparison of FT schemes
PE2
PE1
Bus
P5
P1
P2
P3
P6
P4
1
2
Deadline
100% E0
R=0.999 999 987
PE2
PE1
Bus
P5
P2
P1
P3
P6
1
2
P4
68% E0
R=0.999 999 878
PE2
PE1
Bus
P1
P2
P6
1
P3
P4
2
P5
73% E0
R=0.999 999 920
Straightforward (SS)
Energy optimisation (EO)
Reliable energy optimisation (REO)
RG imposed as hard constraint
PE1
PE2
P1
P2
P3
P4
P5
m1
m2
P6
P
1
10
X
P
2
60
X
P
3
X
40
P
4
40
X
P
5
X
40
PE
1
PE
2
P
6
X
50
k=1
RG=0.999 999 900
66
33
66
33
100
100
PE
1
PE
2
Voltage levels

---
A Constraint Logic Programming Framework
for the Synthesis of Fault-Tolerant
Schedules for Distributed Embedded Systems
Fault-tolerance
Summary
Design optimisation tool for distributed embedded real-time systems
Decides mapping, fault-tolerance policy and fault-tolerant schedule
  - Hard real-time,
  - Hard reliability goal,
  - Static schedule for processes and messages,
  - Fault-tolerance for k transient/soft faults
Optimise for minimal energy consumption
While considering impact of lowering voltages on the probability of faults
Constraint logic programming (CLP) based implementation
Fault-tolerant scheduling
More complex scheduling schemes yield more slack for energy management
  - Trade-off transparency for performance
  - Performance, and hence the obtainable energy savings are greatly increased
More complex schemes demand larger schedule tables to be stored in the processing elements, and more sophisticated online schedulers
Reliable energy management
System reliability is affected by use of energy management
  - The use of DVS increases the probability of faults, thus damaging the system reliability
Reliability must be considered in the optimisation process
  - Considering reliability in the optimisation process allows for finding the minimum energy schedule that meets the reliability goal
  - Reliability is imposed as a constraint
Reliability can be met at very little energy cost
  - Considering the reliability while optimising enables us to find reliable schedules with comparable energy savings
Faults are tolerated by using temporal or spatial redundancy, or a combination of the two
Replication
Re-execution
Energy vs. reliability
Passive Replication
Energy vs. faults
Lowering voltage decreases critical energy of circuit.
Probability of transient faults increase.
Relation is expressed as1:
λ(f)=λ_0 10^{{d(1-f)} over {1-f_{min}} }
Relation between voltage and failure rate1
1 Source: D. Zhu et al.: “Reliability-Aware Energy Management for Periodic Real-Time Tasks”, 2007
IMM / Informatics and Mathematical Modelling Embedded Systems Engineering eselab.imm.dtu.dk
PE2
PE1
P1
P1
PE2
PE1
P1
P1
PE2
PE1
P1
P1
63% E0
PE2
PE1
P1
P3
P5
Bus
1
2
P2
P4
PE2
PE1
P1
P2
P4
P3
P5
Bus
1
2
P3
P4/5
PE2
PE1
P1
P2
P4
P3
P5
Bus
1
2
P1
P2
P4
P3
P5
Fully Transparent Scheduling
Deadline
100% E0
38% E0
Conditional Scheduling
Slack Sharing Scheduling
P1
P2
P3
P4
P5
PE1
PE2
P
1
40
40
P
2
40
40
P
3
30
30
P
4
40
40
P
5
40
40
PE
1
PE
2
m1
m2
k=1
Comparison of FT schemes
PE2
PE1
Bus
P5
P1
P2
P3
P6
P4
1
2
Deadline
100% E0
R=0.999 999 987
PE2
PE1
Bus
P5
P2
P1
P3
P6
1
2
P4
68% E0
R=0.999 999 878
PE2
PE1
Bus
P1
P2
P6
1
P3
P4
2
P5
73% E0
R=0.999 999 920
Straightforward (SS)
Energy optimisation (EO)
Reliable energy optimisation (REO)
RG imposed as hard constraint
PE1
PE2
P1
P2
P3
P4
P5
m1
m2
P6
P
1
10
X
P
2
60
X
P
3
X
40
P
4
40
X
P
5
X
40
PE
1
PE
2
P
6
X
50
k=1
RG=0.999 999 900
66
33
66
33
100
100
PE
1
PE
2
Voltage levels