## Slide 1
Computer Networking: A Top-Down Approach 8th edition Jim Kurose, Keith Ross Pearson, 2020
Course and Exam Review
A note on the use of these PowerPoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
For a revision history, see the slide note for this page.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2020
J.F Kurose and K.W. Ross, All Rights Reserved
Notes: Version History
8.0 (May 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
lighter header font
Updated datacenter slides, day-in-the-life

## Slide 2: Synthesis: a day in the life of a web request
our journey down the protocol stack is now complete!
  application, transport, network, link
putting-it-all-together: synthesis!
  goal: identify, review, understand protocols (at all layers) involved in seemingly simple scenario: requesting www page
  scenario: student attaches laptop to campus network, requests/receives www.google.com

## Slide 3: A day in the life: scenario
Comcast network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
browser
web page
arriving mobile client attaches to network …
requests web page: www.google.com
scenario:
Sounds
simple!

## Slide 4: A day in the life: connecting to the Internet
router has
DHCP server
arriving mobile:
DHCP client
connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP

## Slide 5: A day in the life: connecting to the Internet
router has
DHCP server
arriving mobile:
DHCP client
DHCP
UDP
IP
Eth
Phy
DHCP
UDP
IP
Eth
Phy
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply

## Slide 6: A day in the life… ARP (before DNS, before HTTP)
router has
ARP server
arriving mobile:
ARP client
DNS
UDP
IP
Eth
Phy
Eth
Phy
ARP
before sending HTTP request, need IP address of www.google.com: DNS
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
ARP
ARP reply

## Slide 7: A day in the life… using DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
Comcast network
68.80.0.0/13
DNS
server
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into Comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
demuxed to DNS
DNS replies to client with IP address of www.google.com
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS

## Slide 8: DNS Infrastructure
requesting host
cis.poly.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.poly.edu
1
2
3
4
5
6
authoritative DNS server
dns.cs.umass.edu
7
8
TLD DNS server
Host at cis.poly.edu wants IP address for gaia.cs.umass.edu
Infrastructure:
  Client resolver
  Local DNS server
  Authoritative DNS Server
  Root DNS Server
  Top-Level Domain DNS Server

## Slide 9: Routing and Forwarding
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
Intra-AS
Routing
algorithm
Inter-AS
Routing
algorithm
Forwarding
table
3c
Forwarding table is configured by both intra- and inter-AS routing algorithm
  Intra-AS sets entries for internal dests
  Inter-AS & Intra-As sets entries for external dests

## Slide 10: A day in the life…TCP connection carrying HTTP
DNS
DNS
DNS
Comcast network
68.80.0.0/13
64.233.169.105
Google web server
HTTP
TCP
IP
Eth
Phy
HTTP
to send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in TCP 3-way handshake) inter-domain routed to web server
TCP connection established!
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
web server responds with TCP SYNACK (step 2 in TCP 3-way handshake)

## Slide 11: A day in the life… HTTP request/reply
DNS
DNS
DNS
Comcast network
68.80.0.0/13
64.233.169.105
Google web server
HTTP
TCP
IP
Eth
Phy
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed

## Slide 12: Network View: HTTP and TCP
TCP is a connection-oriented protocol
SYN
SYN/ACK
ACK
GET URL
YOUR DATA HERE
FIN
FIN/ACK
ACK
Web Client
Web Server

## Slide 13: How do we avoid sending too much for the receiver and network to handle?

## Slide 14: TCP Tahoe: Summary
Basic ideas
  Gently probe network for spare capacity
  Drastically reduce rate on congestion
  Windowing: self-clocking
  Other functions: round trip time estimation, error recovery
for every ACK {
if (W < ssthresh) then W++ (SS)
else W += 1/W (CA)
}
for every loss {
ssthresh = W/2
W = 1
}

## Slide 15: Congestion Avoidance Example
Round Trip Times
cwnd (in segments)
Slow Start
cwnd >= ssthresh
cwnd = 1
cwnd = 2
cwnd = 4
cwnd = 8
cwnd = 9
ssthresh = 8

## Slide 16: TCP Reno: Summary
Fast Recovery along with Fast Retransmit used to avoid slow start
On 3 duplicate ACKs
  Fast retransmit and fast recovery
On timeout
  Retransmit last segment and slow start

## Slide 17: Fast Retransmit and Fast Recovery
At steady state, cwnd oscillates around the optimal window size
TCP always forces packet drops
Time
cwnd
Timeout
Slow Start
Congestion Avoidance
Fast Retransmit/Recovery
ssthresh
Timeout

## Slide 18: Example Web Page
Harry Potter Movies
As you all know,
the new HP book
will be out in June
and then there will
be a new movie
shortly after that…
“Harry Potter and
the Bathtub Ring”
page.html
hpface.jpg
castle.gif

## Slide 19
Client
Server
The “classic” approach
in HTTP/1.0 is to use one
HTTP request per TCP
connection, serially.
TCP SYN
TCP FIN
page.html
G
TCP SYN
TCP FIN
hpface.jpg
G
TCP SYN
TCP FIN
castle.gif
G

## Slide 20
Client
Server
Concurrent (parallel) TCP
connections can be used
to make things faster.
TCP SYN
TCP FIN
page.html
G
castle.gif
G
F
S
G
hpface.jpg
S
F
C
S
C
S

## Slide 21
Client
Server
The “persistent HTTP”
approach can re-use the
same TCP connection for
Multiple HTTP transfers,
one after another, serially.
Amortizes TCP overhead,
but maintains TCP state
longer at server.
TCP FIN
Timeout
TCP SYN
page.html
G
hpface.jpg
G
castle.gif
G

## Slide 22
Client
Server
The “pipelining” feature
in HTTP/1.1 allows
requests to be issued
asynchronously on a
persistent connection.
Requests must be
processed in proper order.
Can do clever packaging.
TCP FIN
Timeout
TCP SYN
page.html
G
castle.gif
hpface.jpg
GG

## Slide 23: How do we find a path?

## Slide 24: Routing on a Graph
Goal: determine a “good” path through the network from source to destination
What is a good path?
  Usually means the shortest path
  Load balanced
  Lowest $$$ cost
Network modeled as a graph
  Routers  nodes
  Link  edges
    Edge cost: delay, congestion level, etc.
A
B
C
D
E
F
5
2
3
5
2
1
1
2
3
1

## Slide 25: Intra-domain Routing Protocols
Distance vector
  Routing Information Protocol (RIP), based on Bellman-Ford
  Routers periodically exchange reachability info with neighbors
Link state
  Open Shortest Path First (OSPF), based on Dijkstra
  Each network periodically floods neighbor information to all routers
  Routers locally compute routes

## Slide 26: Hierarchical addressing: route aggregation
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
ISP has an address block; it can further divide this block into sub blocks and assign them to subscriber organizations.

## Slide 27: Example CIDR Routing Table
Address | Netmask | Third Byte | Byte Range
207.46.0.0 | 19 | 000xxxxx | 0 – 31
207.46.32.0 | 19 | 001xxxxx | 32 – 63
207.46.64.0 | 19 | 010xxxxx | 64 – 95
207.46.128.0 | 18 | 10xxxxxx | 128 – 191
207.46.192.0 | 18 | 11xxxxxx | 192 – 255
Hole in the Routing Table: No coverage for 96 – 127
207.46.96.0/19

## Slide 28: Network of networks: BGP and ASes
AS-1
AS-2
AS-3
Interior Routers
BGP Routers

## Slide 29: BGP Relationships
Customer
Provider
Customer pays provider
Peer 1
Peer 2
Peer 3
Peers do not pay each other
Peer 2 has no incentive to route 1 3
Customer
Customer
Provider
$

## Slide 30: Importing Routes
From Provider
From Peer
From Peer
From Customer
ISP Routes

## Slide 31: Exporting Routes
To Customer
To Peer
To Peer
To Provider
Customers get all routes
Customer and ISP routes only
$$$ generating routes

## Slide 32: Also cover many other topics ...
For example …
  Wireless (Ch 7)
  Multimedia networking (Ch 8)
  Network security (Ch 9)

## Slide 33: Wireless Cells
802.11b has 11 channels
Channels 1, 6, and 11 are non-overlapping
Admin chooses frequency for AP

## Slide 34: Wireless Cells
802.11b has 11 channels
Channels 1, 6, and 11 are non-overlapping
Each AP coverage area is called a “cell”
Wireless nodes can roam between cells
AP
AP
AP
AP
AP
AP
Channel 1
Channel 6
Channel 1
Channel 11
Channel 6
Channel 1
Admin chooses frequency for AP
Interference possible: channel can be same as that chosen by neighboring AP!

## Slide 35: HTTP-based Adaptive Streaming (HAS)
HTTP-based streaming
  Video is split into chunks
  Easy firewall traversal and caching
  Easy support for interactive VoD
HTTP-based adaptive streaming
  Multiple encodings of each fragment (defined in manifest file)
  Clients adapt quality encoding based on buffer/network conditions

## Slide 36: HTTP-based Adaptive Streaming (HAS)
HTTP-based streaming
  Video is split into chunks
  Easy firewall traversal and caching
  Easy support for interactive VoD
HTTP-based adaptive streaming
  Multiple encodings of each chunk (defined in manifest file)
  Clients adapt quality encoding based on buffer/network conditions

## Slide 37: HTTP-based Adaptive Streaming (HAS)
HTTP-based streaming
  Video is split into chunks
  Easy firewall traversal and caching
  Easy support for interactive VoD
HTTP-based adaptive streaming
  Multiple encodings of each chunk (defined in manifest file)
  Clients adapt quality encoding based on buffer/network conditions

## Slide 38: HTTP-based Adaptive Streaming (HAS)
HTTP-based streaming
  Video is split into chunks
  Easy firewall traversal and caching
  Easy support for interactive VoD
HTTP-based adaptive streaming
  Multiple encodings of each chunk (defined in manifest file)
  Clients adapt quality encoding based on buffer/network conditions
Chunk1

## Slide 39: HTTP-based Adaptive Streaming (HAS)
HTTP-based streaming
  Video is split into chunks
  Easy firewall traversal and caching
  Easy support for interactive VoD
HTTP-based adaptive streaming
  Multiple encodings of each chunk (defined in manifest file)
  Clients adapt quality encoding based on buffer/network conditions
Chunk1
Chunk2

## Slide 40: HTTP-based Adaptive Streaming (HAS)
HTTP-based streaming
  Video is split into chunks
  Easy firewall traversal and caching
  Easy support for interactive VoD
HTTP-based adaptive streaming
  Multiple encodings of each chunk (defined in manifest file)
  Clients adapt quality encoding based on buffer/network conditions
Chunk1
Chunk2
Chunk3

## Slide 41: HTTP-based Adaptive Streaming (HAS)
HTTP-based streaming
  Video is split into chunks
  Easy firewall traversal and caching
  Easy support for interactive VoD
HTTP-based adaptive streaming
  Multiple encodings of each chunk (defined in manifest file)
  Clients adapt quality encoding based on buffer/network conditions
Chunk1
Chunk2
Chunk4
Chunk3

## Slide 42: HTTP-based Adaptive Streaming (HAS)
HTTP-based streaming
  Video is split into chunks
  Easy firewall traversal and caching
  Easy support for interactive VoD
HTTP-based adaptive streaming
  Multiple encodings of each chunk (defined in manifest file)
  Clients adapt quality encoding based on buffer/network conditions
Chunk1
Chunk2
Chunk4
Chunk3
Chunk5

## Slide 43: Friends and enemies: Alice, Bob, Trudy
well-known in network security world
Bob, Alice (lovers!) want to communicate “securely”
Trudy (intruder) may intercept, delete, add messages
secure
sender
secure
receiver
channel
data, control messages
data
data
Alice
Bob
Trudy

## Slide 44: HTTPS (and TLS/SSL Cipher Suite)
cipher suite
  public-key algorithm
  symmetric encryption algorithm
  MAC algorithm
TLS/SSL supports several cipher suites
negotiation: client, server agree on cipher suite
  client offers choice
  server picks one
CA
Browser
Server

## Slide 45: Exam
State your assumptions
Please explain how you derived your answers. Your final answers should be clearly stated.
Write answers legibly; no marks will be given for answers that cannot be read easily.
Where a discourse or discussion is called for, be concise and precise.
No assistance: closed book, closed notes, and no electronics ...
https://www.ida.liu.se/~TDTS06/exam/index.en.shtml

## Slide 46: Please fill course feedback/Evaliuate