## Slide 1: Reliability-Aware Frame Packing for the Static Segment of FlexRay
Bogdan Tanasa, Unmesh Bordoloi,
Petru Eles, Zebo Peng
Linkoping University, Sweden

## Slide 2: Introduction
Today’s cars are a complex distributed embedded system with multiple electronic components
Automotive electronics are also affected by faults

## Slide 3: Introduction
Some automotive applications are
safety-critical
  Guaranteeing reliability is mandatory
  In-vehicle communication
    Fault Tolerance techniques for reliable communication
  Hard real-time constraints
    End to end deadlines must be satisfied

## Slide 4: Our contribution
Signal packing
  Elementary pieces of information
  Signals will be packed into frames
Reliable frame scheduling over FlexRay based automotive networks
  Via temporal fault-tolerance
    Retransmissions
  At a minimum bandwidth utilization cost

## Slide 5: Why FlexRay ?
Supported by a large consortium
  Car manufacturers
  Automotive suppliers
Hybrid protocol
  FlexRay combines features of time-triggered and event-triggered protocols
    We focus on the Static Segment

## Slide 6: Rest of the talk …
System Model
Signal Packing
Reliability Analysis
CLP-based Formulation
Heuristic Solution
Experimental Results

## Slide 7: System Model
Distributed Automotive Architecture
  set of ECUs E1, E2, … EN
  set of Signals per ECU S = {s1, s2, …, sL}
    Offset
    Period
    Deadline
    Length

## Slide 8: System Model
FlexRay Protocol Parameters
  Length of the Communication Cycle
  Length of the Static Segment
  Number of slots within the Static Segment
1 | 2 | 3 | 4 | 5 | 6 | …
FlexRay Communication Cycle
FlexRay Static Segment
Static Slot

## Slide 9: System Model
FlexRay Frame Format:
Packing more signals into frames help reducing the overhead
Header | Signals | Footer
Overhead

## Slide 10: System Model
Fault Model - The case of transient faults
  Time unit - τ
    Used to define the reliability goal
    Ex: one hour of functionality
  Reliability Goal - ρ
    Imposed by the designer: Ex. ρ = 0.99999
    Maximum number of tolerated faults over a time unit
  Bit Error Rate - BER
    Represents the “quality” of the environment
    Used to compute the probabilities of failures

## Slide 11: Signal Packing
Definition:
Having a set of signals S = {s1, s2, …, sN} build a set of frames F = {f1, f2, …, fM} such that:
- each signal belongs to only one frame
- signals will not violate their deadlines
- frames do not exceed the slot capacity
- the bandwidth used by the set F is minimum

## Slide 12: Signal Packing
Signal | Offset | Period | Deadline | Length
S1 | 0 | 5 | 5 | 16
S2 | 0 | 2 | 2 | 32
S3 | 0 | 3 | 3 | 64
… |  |  |  | 
SN | 0 | 10 | 10 | 54
The signal with the minimum period imposes the period of the resulting frame
The deadline of the resulting frame must be computed such that the deadlines of the initial signals will not be violated
F | 0 | 2 | ? | 112

## Slide 13: Signal Packing
Example
Signal | Offset | Period | Deadline | Length
S1 | 0 | 3.00 | 2.00 | 16
S2 | 0 | 2.00 | 1.50 | 24
F | 0 | 2.00 | ? | 40
 | 0 |  | 1.5 | 2 |  | 3 | 3.5 | 4 |  | 5 | 5.5 | 6
2.00 – 1.00 = 1.00
Waiting time
S2
S1
F
S1S2
S2
S1S2
Remaining time
Slack

## Slide 14: Signal Packing
General Case:
  gcd – Greatest Common Divisor

## Slide 15: How packing signals affects the schedulability?
Period | Deadline
6 | 6
7 | 7
12 | 12
Frame:
Period: T = 6
Deadline: D = 2
Frame:
Period: T = 6
Deadline: D = 6
FC = 5 ms |  |  | ST = 2 ms |  |  | NS = 2 slots |  | 
1 | 2 | DYN | 1 | 2 | DYN | 1 | 2 | DYN
0 |  | 2 |  |  | 5 | 6 |  | 8 |  | 10 |  | 12 |  | 14
Deadline violation!

## Slide 16: How packing signals affects the schedulability?
Period | Deadline
6 | 6
7 | 7
12 | 12
Frame:
Period: T = 6
Deadline: D = 6
FC = 5 ms |  |  | ST = 2 ms |  |  | NS = 2 slots |  | 
1 | 2 | DYN | 1 | 2 | DYN | 1 | 2 | DYN
0 |  |  |  |  | 5 | 6 |  |  |  | 10 |  | 12 |  | 
1 | 2 | DYN
15 |  |  | 18 |  |  | 
Schedulable using the second slot!

## Slide 17: Reliability Analysis
For a given packing of signals into frames the required number of retransmissions has to be computed
Based on:
  period of frames
  probabilities of failure of each frame in part
  time unit
  reliability goal

## Slide 18: Reliability Analysis
The particular case of one frame
Probability to have the initial transmission faulty:
Probability to have k consecutive retransmissions faulty:
Probability to have at least one successful transmission in the case of k consecutive retransmissions for one instance:
Probability to have at least one successful transmission in the case of k consecutive retransmissions for all instances over a time unit:
1
2
4
3

## Slide 19: Reliability Analysis
The general case of more then one frame
Assumptions :
Different messages can be retransmitted for different number of times
Faults in messages are independent events
The probability to have at least one successful transmission for all instances of all messages:

## Slide 20: Reliability Analysis
Solve:
  pi = probability of failure of frame Fi
    Based on Bit Error Rate - BER and length - Wi
  Ti = period of frame Fi
  ki = the required number of retransmissions of frame Fi
    Directly impacts the bandwidth
  τ = time unit
  ρ = reliability goal
The reliability goal must be satisfied with a minimum cost in terms of bandwidth utilization:

## Slide 21: Why it is important to consider fault tolerance requirments while packing?
Signals | Offset | Period | Deadline | Length
S1 | 1 | 8 | 8 | 20
S2 | 1 | 8 | 8 | 15
S3 | 2 | 4 | 4 | 20
S4 | 1 | 12 | 12 | 25
S5 | 2 | 12 | 12 | 20
S6 | 1 | 16 | 16 | 14
Method 1:
Pack signals first and after that apply fault tolerance technique
Output:
Only one frame which requires 10 slots
(S1 ... S6) | 1 | 4 | 4 | 114

## Slide 22: Why it is important to consider fault tolerance requirments while packing?
Signals | Offset | Period | Deadline | Length
S1 | 1 | 8 | 8 | 20
S2 | 1 | 8 | 8 | 15
S3 | 2 | 4 | 4 | 20
S4 | 1 | 12 | 12 | 25
S5 | 2 | 12 | 12 | 20
S6 | 1 | 16 | 16 | 14
Method 2:
Consider fault tolerance requirments while packing
Output:
Two frames which requires 9 slots in total
(S1 S2 S3) | 2 | 4 | 4 | 55
(S4 S5 S6) | 1 | 12 | 12 | 59

## Slide 23: Problem Formulation
Each ECU generates a set of signals
For all sets of signals find a set of frames such that:
  The reliability goal is satisfied
  Slots can be assigned to frames such that the deadlines are satisfied
    Signals don’t miss their deadlines
  Bandwidth utilization is minimum

## Slide 24: CLP-based Formulation
Signal params
Packing rules
FlexRay params
Reliability goal
Input
A set of packed frames that are fault tolerant and schedulable
Output
Solver
(CLP based)
Optimization objective
Minimize the total number of used slots
Reliability constraints
Scheduling constraints

## Slide 25: CLP-based Formulation
A schedule represents an assignment of final frames to slots
Scheduling constraints
  All instances of a given frame have to accommodate k retransmissions before the deadline

## Slide 26: Heuristic Solution
ECU1
ECUi
...
ECUN
...
Compute the required number of retransmissions
Reliability Analysis
Initial: Each signal is a frame
  Solve:
  Relax the integrality constraint
  Impose ∇F = 0 (first order optimality condition)
  Obtain in general non-integer values of ki

## Slide 27: Heuristic Solution
ECU1
ECUi
...
ECUN
...
Compute the required number of retransmissions
Reliability Analysis
Initial: Each signal is a frame
For each ECU
Input: Set of frames
Goal: Find the best pair of frames based on the packing metric
Output: A new set of frames

## Slide 28: Heuristic Solution
Step 2: Packing Metric
  Input: F = {f1, f2, …, fL} – set of frames
  Find: fu ● fv, u ≠ v – the best pair of frames which minimize the bandwidth
  Tuv = min{Ti}
  Duv = min{Di – Tuv + gcd(Tuv, Ti)}
  Wuv = Wi+Wj
  Kuv ≥ max{Ki, Kj}
Packing of signals into frame
The required number of retransmissions
Approximate Kuv
Try to fill the frames which have large periods
Try to keep large deadlines while increasing the value of K by very little

## Slide 29: Heuristic Solution
Step 3: Build a fault tolerant static schedule
  Called with the ceiling values of ki
  Find an assignment of slots to the final frames
Step 4: Remove signals from frames to increase the deadlines
  Detect the signal which provides two frames with the highest possible deadlines
  Recall step 1 and step 3

## Slide 30: Experimental Results
Two set of experiments
  Small test cases
    Compare the heuristic with results provided by the optimal CLP implementation
  Large test cases
    Compare the heuristic against the traditional method when fault tolerant requirements are applied after packing the signal into frames

## Slide 31: Experimental Results
Small test cases
Our heuristic was in average only 15 % far from the optimal solution

## Slide 32: Experimental Results
Large test cases
  Our method vs. traditional method
    First pack the signal into frames
    Second apply fault-tolerance techniques
  In average the improvement is around 30% in terms of bandwidth utilization

## Slide 33: Experimental Results
Chart: Number of ECUs
| 5 | 10 | 15 | 20
RAFP | 50 | 107 | 163 | 278
3 Step | 75 | 143 | 226 | 350

## Slide 34: Conclusions
A method for packing signals into frames with fault tolerance requirements was presented
  The required number of retransmissions is computed
  An fault tolerant schedule for the Static Segment is constructed
Message:
The fault tolerance requirments need to be considered while packing to achive
good bandwidth utilization

## Slide 35: Thank you!

## Slide 36: Heuristic Solution
Input: F = {f1, f2, …, fL} – set of frames
Find: fu ● fv, u ≠ v – the best pair of frames based on packing metric
Explore L x (L – 1) / 2 pairs
Output: F’ = F – {fu, fv} U {fuv}
ECU1
ECUi
...
ECUN
...
Compute the required number of retransmissions
Build a fault tolerant schedule for the resulted frames
1
3
2
Pack frames for ECUi
Relax deadlines if needed
4
Reliability Analysis
Evaluate the bandwidth consumption
Go to Step 1
Extract signals from frames to increase the deadlines
Initial: Each signal is a frame