## Slide 1: Scheduling for Fault-Tolerant Communication on the Static Segment of FlexRay
Bogdan Tanasa, Unmesh D. Bordoloi,
Petru Eles, Zebo Peng
Department of Computer and Information Science,
Linkoping University, Sweden
December 3, 2010

## Slide 2: Introduction
Today’s cars are a complex distributed embedded system with multiple electronic components
Automotive electronics are also affected by faults
[Corno et. al. 2004, Zanoni et. al. 1993]

## Slide 3: On the other hand …
Automotive applications are safety-critical
  Guaranteeing reliability is mandatory
    No room for errors whatever may be the cause
  Hard real-time constraints

## Slide 4: Our contribution
We focus on in-vehicle communication
Reliable message scheduling over FlexRay based automotive networks
  Via temporal fault-tolerance
    Retransmissions
  At a minimum bandwidth utilization cost

## Slide 5: Why FlexRay ?
Supported by a large consortium
  Car manufacturers
  Automotive suppliers
Expected to become the de facto standard in automotive communication
Hybrid protocol
  FlexRay combines features of time-triggered and event-triggered protocols
    We focus on the Static Segment

## Slide 6: Rest of the talk …
System Model
Reliability Analysis
Motivational Example
CLP-based Formulation
Heuristic Solution
Experimental Results
Conclusions

## Slide 7: System Model
1. Messages | 2. FlexRay Protocol | 3. Fault Model
Offset | Length of the FlexRay cycle | Time unit
Period | Length of the Static Segment | Reliability goal
Deadline | Number of available slots | Bit Error Rate
Length |  | Probability of failure
1 | 2 | 3 | 4 |  | 1 | 2 | 3 | 4 |  | 1 | 2 | 3 | 4 |  | 1 | 2 | 3 | 4 |  | 1 | 2 | 3 | 4 |  | 1 | 2 | 3 | 4 | 
Length of the FlexRay Cycle
Length of the Static Segment
Static Slots
Length of the Dynamic Segment

## Slide 8: System Model
FlexRay Bus
ECU1
ECU2
ECUM
The case of transient faults
Temperature variation
Electromagnetic interferences
Radiations
3. Fault Model
Time unit
Reliability goal
Bit Error Rate
Probability of failure
BER

## Slide 9: Reliability Analysis
The particular case of one message
Probability to have the initial transmission faulty:
Probability to have k consecutive retransmissions faulty:
Probability to have at least one successful transmission in the case of k consecutive retransmissions for one instance:
Probability to have at least one successful transmission in the case of k consecutive retransmissions for all instances over a time unit:
1
2
4
3

## Slide 10: Reliability Analysis
The general case of more then one message
Preliminaries :
Different messages can be retransmitted for different number of times
Faults in messages are independent events
The probability to have at least one successful transmission for all instances of all messages:

## Slide 11: Reliability Analysis
Problem: What are the minimum number of retransmissions which have to be performed for each message in part such that the reliability goal is achieved?

## Slide 12: Motivational Example
2
time (ms)
0
3
2
4
6
2
Cycle 1
Cycle 2
Cycle 3
M2: T = 2, D = 0.4, p = 0.4
M1: T = 3, D = 2.5, p = 0.6
FC = 2, ST = 2, NS = 5
= 6, = 0.09
2 utilized slots
(1-p1)2 x (1-p2)3 = 0.034 < 0.09
4 utilized slots
(1 – p31)2 x (1 – p2)3 = 0.131 > 0.09
21
1
2
21
1
11
12
11
12
2
21
3 utilized slots
(1 – p1)2 x (1 – p22)3 = 0.094 > 0.09

## Slide 13: Motivational Example
2
time (ms)
0
3
2
4
6
2
Cycle 1
Cycle 2
Cycle 3
M2: T = 2, D = 0.4, p = 0.4
M1: T = 3, D = 2.5, p = 0.6
FC = 2, ST = 2, NS = 5
= 6, = 0.09
21
2
21
2
21
3 utilized slots
(1 – p1)2 x (1 – p22)3 = 0.094 > 0.09
0.4
0.4
0.4
1
1

## Slide 14: CLP-based Formulation
Message params
FlexRay params
Reliability goal
Input
Fault tolerant schedule
Output
Solver
(CLP based)
Optimization objective
Minimize the total number of used slots
Reliability constraints
Scheduling constraints

## Slide 15: CLP-based Formulation
A schedule represents an assignment of messages to slots
Scheduling constraints
  All instances of a given message have to accommodate k retransmissions until the deadline
  Sharing slots between messages is not allowed
  Ensuring the temporal order of retransmissions

## Slide 16: Heuristic Solution
Get the required number of retransmissions
Failure
Feedback Loop
Final output
Get the schedule
Stage II
Identify critical messages
Stage III
Get the required number of retransmissions
Stage I

## Slide 17: Heuristic Solution Stage I
  Lower bound
  The minimum number of retransmissions is defined as the smallest k for which:
  Particular case:

## Slide 18: Heuristic Solution Stage I
Definition: A group is a set of messages which can satisfy the reliability goal using the lower bounds
Greedily build groups of messages which satisfy the reliability goal
Combine the groups to reach the global goal

## Slide 19: Heuristic Solution Stage I
Example:
Message | Period | Deadline | Length | Lower bound | Reliability
M1 | 5 | 3 | 32 | 1 | X
M2 | 15 | 10 | 64 | 2 | 
M3 | 20 | 15 | 24 | 1 | 
M4 | 8 | 6 | 128 | 2 | 
M5 | 16 | 10 | 64 | 2 | 
M6 | 32 | 16 | 64 | 1 | 
Group 1 | Group 2 | Group 3
M1 M3 M6 | M2 M5 | M4
Reliability |  | 

## Slide 20: Heuristic Solution Stage II
Get the schedule
Get the schedule
Get the required number of retransmissions
Stage I
Failure
Feedback Loop
Final output
Identify critical messages
Identify critical messages
Stage III
Stage II

## Slide 21: Heuristic Solution Stage III
Once the values of k are computed the scheduler is invoked (Stage II)
Identify messages which might have created bottlenecks
  Based on the scheduling constraints
Formulated as a CLP problem
  Heuristic search based on the limited discrepancy search algorithm

## Slide 22: Heuristic Solution Stage III
Search space for Stage III
1
2
1
1
2
2
3
1
3
4
4
5
3
Values given by Stage I
Lower bounds
k*
k*
Minimize:

## Slide 23: Heuristic Solution Stage III
Example
Message | Period (ms) | Deadline (ms) | Length (bits)
M1 | 5 | 4.5 | 96
M2 | 3.5 | 3.0 | 128
M3 | 2.5 | 2.0 | 64
M4 | 10 | 10 | 32
Lower bounds | k
1 | 2
2 | 3
1 | 2
1 | 1
Reliable | 
Schedulable?
X
X
Stage I
Stage II
Lower bounds | k
1 | 2
2 | 2
1 | 2
1 | 1
Reliable | 
Stage III
Schedulable ?
Message | Period (ms) | Deadline (ms) | Length (bits)
M1 | 5 | 4.5 | 96
M2 | 3.5 | 3.0 | 128
M3 | 2.5 | 2.0 | 64
M4 | 10 | 10 | 32
Lower bound | k
1 | 2
2 | 2
1 | 2
1 | 3
Reliable | 
Recall Stage I for M1, M3, M4
Who is responsible for the fact that M2 and M4 are NOT schedulable?
M2 is responsible !

## Slide 24: Experimental Results
3 methods are compared:
  Optimal-CLP
    The CLP-based formulation
  H-CLP
    Heuristic approach for computing the required number of retransmissions
    Optimal implementation of message scheduling (Stage II)
  H-H
    Heuristic approach for computing the required number of retransmissions
    Heuristic approach for obtaining the schedule

## Slide 25: Experimental Results
Small test cases
  The CLP formulation runs in reasonable amount of time and the optimal solution is provided
93%

## Slide 26: Experimental Results
Large test cases
  The CLP formulation is NOT able to run and the optimal solution is NOT provided
95%

## Slide 27: Conclusions
A method for synthesizing reliable schedules on the FlexRay bus has been presented:
  Number of needed retransmissions is determined
  For each message and retransmission a slot is assigned
Easy to generalize the proposed method to classes of messages with different reliability constraints

## Slide 28: Thank you!

## Slide 29: Heuristic Solution Stage I
Compute the lower bounds
Sort the messages in
the decreasing order
of the PSi values
Identify the biggest group for which:
Update the reliability goal
Recursively call the algorithm for the
remaining messages
1
2
3
4
5
The worst case time complexity:
O(N2 log N)

## Slide 30: Heuristic Solution
The addressed problem is NP-complete
  Efficient heuristic is needed
A 3 stage approach
  Identify the required number of retransmissions
    Reliability analysis
  Test the scheduling constraints
  Feedback loop
    Identify critical messages

## Slide 31: Heuristic Solution Stage III
Messages for which are declared to be critical
  The lower bound will be used for them
  Recall Stage I for the remaining messages
Stops when:
  the schedule is build, or
  the method cannot identify any other critical messages
    Critical messages cannot form a group