## Slide 1: TDTS11 Computer Networks and Internet Protocols
Gurjot Singh Gaba
January 2024
First part adapted from slides by
J.F. Kurose and K.W. Ross, © 1996–2020

## Slide 2: Contact information
Gurjot Singh Gaba
gurjot.singh@liu.se (begin with ”TDTS11” in the email subject)

## Slide 3: Overview of lessons / labs
TDTS11 Protocol Layers & Wireshark
Two lessons to introduce the different labs
  First lesson introduces protocol layers & Wireshark (assignment 1–3)
  Second lesson introduces scripts (assignment 4)
Nine* lab sessions with a total of 4 assignments
Please note that lab 4 is time-consuming, so follow the recommended deadlines
3

## Slide 4: Protocol Layers
An introduction to Internet and protocol layers

## Slide 5: Protocols
TDTS11 Protocol Layers & Wireshark
5
Hi
Hi
Got the time?
TCP connection response
Get https://www.ida.liu.se/~TDTS11/
<file>
time
TCP connection request
2:00

## Slide 6: What’s the Internet: “nuts and bolts” view
TDTS11 Protocol Layers & Wireshark
Billions of connected devices:
hosts = end systems
running network apps at Internet’s “edge”
Packet switches: forward packets (chunks of data)
routers, switches
Communication links
fiber, copper, radio, satellite
transmission rate: bandwidth
Networks
collection of devices, routers links: managed by an organization
6
Internet
mobile network
home network
enterprise
network
national or global ISP
local or
regional ISP
datacenter network
content provider network

## Slide 7: What’s the Internet: “nuts and bolts” view
TDTS11 Protocol Layers & Wireshark
Interconnected ISPs
Protocols are everywhere
  control sending, receiving of messages
  e.g., HTTP (Web), streaming video, Skype, TCP, IP, WiFi, 4G, Ethernet
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
7
enterprise
network
national or global ISP
local or regional ISP
datacenter network
content provider network
home network
HTTP
Ethernet
Skype
IP
WiFi
mobile network 4G
Internet: “network of networks”
TCP
Streaming video

## Slide 8: Internet protocol stack
TDTS11 Protocol Layers & Wireshark
application: supporting network applications
  FTP, SMTP, HTTP, DNS, DHCP
transport: process-process data transfer
  TCP, UDP, ICMP, IGMP, NAT
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), PPP, HDLC, X.25
physical: bits “on the wire” Bluetooth, PON, DSL, IEEE.802.11, IEEE.802.3
8
application
transport
network
link
physical

## Slide 9: Encapsulation
TDTS11 Protocol Layers & Wireshark
9
HTTP [data]
GET /somedir/page.html HTTP/1.1 Host: www.someschool.edu
…
For better understanding, let us watch this video

## Slide 10: Encapsulation
TDTS11 Protocol Layers & Wireshark
10
Bits | 
Ethernet [frame] Destination address Source address … | 
IP [packet] Destination address Source address … | 
TCP [segment] Destination port Source port … | HTTP [data] GET /somedir/page.html HTTP/1.1 Host: www.someschool.edu …
application
transport
network
link
physical

## Slide 11: Wireshark
An introduction to the network protocol analyzer Wireshark

## Slide 12: What is Wireshark?
TDTS11 Protocol Layers & Wireshark
”Wireshark is the world’s foremost and widely-used network protocol analyzer.” (according to themselves)
Multi-platform packet analyzer, used for capturing, viewing and analyzing network packages
Free and open-source, available at https://www.wireshark.org
12

## Slide 13: Limitations of Wireshark on school computers
TDTS11 Protocol Layers & Wireshark
Because administrator privileges is needed to capture network traffic, you won’t be able to capture traffic on university computers (same goes for ThinLinc)
For all assignments, except the 4th, trace files are provided. Those can be opened and analyzed without limitations on university computers.
However, it’s highly recommended to download Wireshark and do as much of network capturing as possible yourselves to gain a better understanding.
13

## Slide 14: Start screen of Wireshark
TDTS11 Protocol Layers & Wireshark
Latest version of Wireshark (4.0.2)
Should be reasonably up to date on university computers, but it often preferred to work on own computer.
Let’s you select interface for capturing (normally Wi-Fi or Ethernet), or allows you to open trace files
14

## Slide 15: Wireshark’s GUI
TDTS11 Protocol Layers & Wireshark
Shortcuts
Display filter
Listing of captured packets
Details of selected packet header
Packet content in hexadecimal and ASCII
15

## Slide 16: Visible headers
TDTS11 Protocol Layers & Wireshark
Depending on the packet/protocol type, you will see different protocol data in the expanded view
Starts with “lowest” level (physical) and is followed by link, network, transport and application layer
“Highest” level is displayed as protocol in the packet view, but all is visible in the detailed view
16

## Slide 17: Tips & tricks
TDTS11 Protocol Layers & Wireshark
Data contained in [square brackets] are calculated/presented by Wireshark and are not part of the actual data, and will not always be accepted as answers
You can right click fields in the packet listing and apply as a filter (i.e. a given destination IP address will apply “ip.dst == ” followed by that IP address as filter
Ctrl/Cmd + M will mark (select) packets
17

## Slide 18: Traceroute
A brief introduction to assignment 3

## Slide 19: Traceroute
TDTS11 Protocol Layers & Wireshark
Traceroute is a program used for sending datagrams of different sizes to a destination to calculate RTT and hop distance
Mac/Unix/Linux only. For Windows alternatives, see assignment 3 text
Uses ICMP (Internet Control Message Protocol) on the IP layer. Make sure you understand it before starting assignment 3
19

## Slide 20: Assignments

## Slide 21: Assignments
TDTS11 Protocol Layers & Wireshark
Assignment 1: “Wireshark lab: Getting started + HTTP”
  1+ time slot, plus own work (deadline January 28)
Assignment 2: “Wireshark lab: TCP”
  1+ time slots, plus own work (deadline February 4)
Assignment 3: “Wireshark lab: IP”
  1+ time slot, plus own work (deadline February 12)
Assignment 4: “Web analysis”
  4+ to 5+ time slots, plus own work (deadline March 8-9)
  Introductory teaching session February 15
21

## Slide 22: Questions?
gurjot.singh@liu.se (subject “TDTS11 […]”)
or general questions in Teams!
www.liu.se