## Slide 1: OpenModelica OMShell and OMNotebook Introduction and Exercises
Peter Fritzson, Adrian Pop, Peter Aronsson OpenModelica Course at INRIA, 2006 06 08

## Slide 2: OMShell and OMNotebook OpenModelica End-User Subsystems
OMShell – interactive session handler for Modelica scripting
OMNotebook – interactive electronic notebook for Modelica teaching (with DrModelica), scripting, and documentation
OpenModelica Compiler (OMC) – compiles and executes/simulates Modelica models
ptplot package (from Berkeley) make plots

## Slide 3: OpenModelica Environment Architecture

## Slide 4: Interactive Session Handler – on dcmotor Example (Session handler called OMShell – OpenModelica Shell)
>>simulate(dcmotor,startTime=0.0,stopTime=10.0)
>>plot({load.w,load.phi})
model dcmotor
Modelica.Electrical.Analog.Basic.Resistor r1(R=10);
Modelica.Electrical.Analog.Basic.Inductor i1;
Modelica.Electrical.Analog.Basic.EMF emf1;
Modelica.Mechanics.Rotational.Inertia load;
Modelica.Electrical.Analog.Basic.Ground g;
Modelica.Electrical.Analog.Sources.ConstantVoltage v;
equation
connect(v.p,r1.p);
connect(v.n,g.p);
connect(r1.n,i1.p);
connect(i1.n,emf1.p);
connect(emf1.n,g.p);
connect(emf1.flange_b,load.flange_a);
end dcmotor;

## Slide 5: Event Handling by OpenModelica – BouncingBall
>>simulate(BouncingBall,
stopTime=3.0);
>>plot({h,flying});
model BouncingBall
parameter Real e=0.7 "coefficient of restitution";
parameter Real g=9.81 "gravity acceleration";
Real h(start=1) "height of ball";
Real v "velocity of ball";
Boolean flying(start=true) "true, if ball is flying";
Boolean impact;
Real v_new;
equation
impact=h <= 0.0;
der(v)=if flying then -g else 0;
der(h)=v;
when {h <= 0.0 and v <= 0.0,impact} then
v_new=if edge(impact) then -e*pre(v) else 0;
flying=v_new > 0;
reinit(v, v_new);
end when;
end BouncingBall;

## Slide 6: Run Scripts in OpenModelica
RunScript command interprets a .mos file
.mos means MOdelica Script file
Example: >> runScript("sim_BouncingBall.mos")
loadFile("BouncingBall.mo");
simulate(BouncingBall, stopTime=3.0);
plot({h,flying});
The file sim_BouncingBall.mos :

## Slide 7: Some OMShell Exercises
Start OMShell (e.g. from the start menu)
Look at the examples in the OpenModelicaUsersGuide.
Try evaluating a small expression, e.g. 2+3, push return
type help()
try command completion, e.g. type loadM followed by tab
fill in Modelica (i.e. loadModel(Modelica))
Use the file menu->LoadModel and load the dcmotor (../testmodels)
type sim followed by tab; fill in dcmotor
type plot followed by tab; fill in some variable(s) to plot (look at the users guide)
type in a small function and call it

## Slide 8: OpenModelica OMNotebook Electronic Notebook with DrModelica
Primarily for teaching
Interactive electronic book
Platform independent
OMNotebook Does not need Mathematica

## Slide 9: Interactive Contents in DrModelica Contains Examples and Exercises from Modelica Book
Recent Book, 2004:

## Slide 10: Cells with both Text and Graphics
Java must be installed for plotting to work

## Slide 11: Exercises and Answers in OMNotebook DrModelica

## Slide 12: Some OMNotebook Commands (see also OpenModelica Users Guide)
Shift-return (evaluated a cell)
File Menu (open, close, etc.)
Text Cursor (vertical), Cell cursor (horisontal)
Cell types: text cells & executable code cells
Copy, paste, group cells
Copy, pase, group text
Command Completion (shift-tab)

## Slide 13: Simplest Model – Hello World!
A Modelica “Hello World” model
class HelloWorld "A simple equation"
Real x(start=1);
equation
der(x)= -x;
end HelloWorld;
Equation: x’ = - x
Initial condition: x(0) = 1
Simulation in OpenModelica environment
0.5
1
1.5
2
0.2
0.4
0.6
0.8
1
simulate(HelloWorld, stopTime = 2)
plot(x)

## Slide 14: Example class: Van der Pol Oscillator
-1
1
2
-2
-1
1
2
-2
class VanDerPol "Van der Pol oscillator model"
Real x(start = 1) "Descriptive string for x"; // x starts at 1
Real y(start = 1) "y coordinate"; // y starts at 1
parameter Real lambda = 0.3;
equation
der(x) = y; // This is the 1st diff equation //
der(y) = -x + lambda*(1 - x*x)*y; /* This is the 2nd diff equation */
end VanDerPol;
simulate(VanDerPol,stopTime = 25)
plotParametric(x,y)

## Slide 15: Small OMNotebook Exercise
Locate the HelloWorld model in DrModelica using OMNotebook!
Simulate and plot the example. Do a slight change in the model, re-simulate and re-plot.
class HelloWorld "A simple equation"
Real x(start=1);
equation
der(x)= -x;
end HelloWorld;
simulate(HelloWorld, stopTime = 2)
plot(x)
Locate the VanDerPol model in DrModelica and try it!
Do some change and re-simulate

## Slide 16: Small OMNotebook Exercises cont.
Select and copy a cell (tree to the right)
Position the horizontal cell cursor: first click between cells; then click once more on top of the horizontal line
Paste the cell
Note: You can find most Users Guide examples in the UsersGuideExamples.onb in the testmodels directory